## Slide 1
Jun 16, 2025
D. Ratner
SLAC National Accelerator Laboratory
Coincident anomaly detection for a particle accelerator

## Slide 2
Introduction to X-ray Free-Electron Lasers (XFELs)
Suga et al.
Photosystem II
Shock waves in extreme conditions
Milathianaki et al.
Si
Ekeberg et al.,
Single particle imaging (Mimivirus)
X-ray free-electron lasers: Accelerator driven x-ray sources to study ultrafast, ultrasmall scale phenomena

## Slide 3
Introduction to X-ray Free-Electron Lasers (XFELs)
X-ray free-electron lasers: Accelerator driven x-ray sources to study ultrafast, ultrasmall scale phenomena
X-ray FELs are instabilities, i.e. sensitive to operational conditions
 AI efforts target:
Tuning
Anomalies
2x longer gainlength
100x drop in power
FEL gain curve

## Slide 4: Motivation
SLAC Linear Accelerator and 280 Overpass
SLAC RF Stations
Failure prediction at accelerators:
Failures cause downtime, degrade performance
1000s of subsystems  frequent failures
200k variables to monitor at LCLS  impossible to do manually
Big data, but nearly none of it labeled

## Slide 5: Anomaly Detection: RF Station Faults
Anomaly detection at an X-ray Free-Electron Laser
Highway 280
RF stations
Case study: RF station faults
RF stations provide power for acceleration
Most common fault at LCLS (1000s/year)
Existing algorithm has too many false positives  operators ignore alarms
70% missed faults (i.e. poor recall)
70% of alarms are false (i.e. poor precision)
Recall = TP/(TP+FN) Precision = TP/(TP+FP)
TP = true positive, FP = false positive, FN = false negative

## Slide 6: Anomaly Detection: RF Station Faults
Operators watch for a drop in X-ray power here
After observing a drop, search for RF stations with warning/fail status
Actual existing solution: Manual, beam-based anomaly detection
Many missed events
(recall ~ 1%)

## Slide 7: Anomaly Detection: RF Station Faults
New approach: Beam-based algorithm inspired by operators
Highway 280
Algorithm #1 looks for subsystem anomalies
RF stations
Beam position monitors
Algorithm #2 looks at final beam quality
Simultaneous anomalies trigger alarm
Question: How do we assess these algorithms with no labels?
 self-consistency!

## Slide 8: Coincident Anomaly Detection (CoAD)
Consider two algorithms making predictions on two streams of data
Subsystem
Beam quality
Algorithm 1
Algorithm 2
Prediction 2
Unknown
machine state
Red stars = consistent
black stars = inconsistent
More red = higher recall;
less black = higher precision
FP rate = product of black star rates
TP rate = red star rate – FP rate
Prediction 1
Self-Consistency
metric
 Unsupervised precision/recall
Threshold
R. Humble et al., MLST (2024)

## Slide 9: Coincident Anomaly Detection (CoAD)
Consider two algorithms making predictions on two streams of data
We estimate unlabeled version of recall/precision from coincidence
Estimates can be differentiable  can train neural networks!
i.e. a loss function, not just a metric
Formally the loss function is defined for NN outputs :
: Estimated anomaly rate
: Weighting factor (recall vs. precision)
: red star rate
: estimated FP rate
R. Humble et al., MLST (2024)

## Slide 10: CoAD for RF Station Faults
RF Station data
Beam Data
Estimated precision/recall
Implementation for RF station task:
Network 1
Network 2
Unsupervised loss function
Anomaly confidence
Anomaly confidence
Normal examples
Anomalous examples
Jason Liang
RF station phase
RF station phase
Beam energy
Beam energy

## Slide 11: CoAD for RF Station Faults
 | Precision | Recall (events)
Manual recording by operator | NA | 6
Status bit | 0.31 | 385
Coincident Detection | 0.88 | 504
6x fewer false positives vs. status bit
100x more anomalies vs. manual recording
30% more anomalies vs. status bit
Summary of predictions on 4 months of data
Ryan Humble, Finn O’Shea, Zhe Zhang, Jason Liang
R. Humble et al., PRAB (2022)
R. Humble et al., MLST (2024)
With phase data,
Now 4x higher recall!

## Slide 12: CoAD for RF Station Faults
Interpretability and root-cause analysis
Modulator fault (EVO)
Water fault (WSF)
Rich phase data  can cluster faults and map to known problems
Interpretability of scores  can investigate failure modes of the models
Jason Liang

## Slide 13: CoAD for RF Station Faults
Interpretability and root-cause analysis
Rich phase data  can cluster faults and map to known problems
Interpretability of scores  can investigate failure modes of the models
Jason Liang

## Slide 14: Other applications of CoAD
Searching for edge-localized modes (ELMs) in tokamaks
Fusion-cdt
”S” network sees filterscope/interferometer
“Q” network sees beam-emission spectrum (BES)
Finn O’Shea, Ryan Coffee, et al., MLST (2024)
Finding instabilities in Tokamaks
Failures in milling equipment
Removing backgrounds from Lux-Zeppelin
Template-free search at LIGO
CoAD finds 50% more ELMs than SoTA!
Exploring new applications:
Let me know if you have an idea!

## Slide 15
Thanks for your attention!
And thanks to collaborators:
Eric Darve, Ryan Humble, Jason Liang, Finn O’Shea, Zhe Zhang